## Slide 1: Major Project
Group D

## Slide 2: Design Objectives
Our primary objectives for this project are as follows:
Create a technology to improve easy of use for modern supermarkets,
Implement a modular design to allow better scalability and maintenance.

## Slide 3: Technology concept

## Slide 4: Industry Need for Concept

## Slide 5: Documentation
Our project has been created and documented through GitHub:
  Each group meeting has a minutes document
  Project itself is outlined in README document.

## Slide 6: Project Timeline
Scheduled timeline for project

## Slide 7: Module Design
Our project has been split into five modules:
Serial module: handles error outputs, user queries and outputs corresponding messages
Sound & visual module: flashes and beeps corresponding to user distance from system
Status module: monitors orientation and acceleration of system
Object detection module: detects an object in front of the system
Tracking module: tracks position of object

## Slide 8: Module Interface and Free Body Diagram
Module | Inputs | Outputs
Serial Module | Queries User angle/distance Error messages | Error Messages Angle/distance
Audio/Visual Module | User distance | Sound/lights
Status Module | Gyroscope values Accelerometer values | System orientation System acceleration
Object Detection Module | LIDAR values System orientation | Object position
Object Tracking Module | Object position | User angle/distance

## Slide 9: Roles and Responsibilities
Roles for this project were spread evenly among the group, with each member acting as the primary for one module.
Roles | Primary | Secondary | Support
Serial module | Will | Joon | 
Audio/visual module | Ethan |  | 
Status module | Joon |  | 
Object tracking module | Taj | Josh | 
Object detection module | Josh | Taj | 
Documentation | Will | Ethan | 

## Slide 10: Serial Module PSEUdoCode
Serial Output
Function called
Load argument into buffer and end buffer with null
Update message to send bit/register to true
Check whether terminal ready to receive
If ready to receive, transmit character by character until null reached Update message to send bit/register to false
Clear buffer
Serial Input
If receive interrupt triggered
While message waiting to be received, read character by character into buffer
Update message to receive bit/register to false once null character received

## Slide 11: AUDIO/Visual Module PseudoCode
Sound Module
Take in distance b/w cart and user (maybe via function call)
If user is too close beep
  Beep at variable lengths based on distance
Visual Module
Take in distance b/w cart and user (maybe via function call)
Convert integer values to array of digits example:
  (assumed max distance = 40m, therefore max digits = 2)
  Distance = 2, array = [0, 2], displayed “02”
  Distance = 13, array = [1,3], displayed “13”
Convert to seven seg values
Send to 7-seg display

## Slide 12: Status Module PseudoCode

## Slide 13: Object Detection PseudoCOde

## Slide 14: Object Tracking PseudoCode

## Slide 15: Technology Demonstration

## Slide 16: Scalability and Further Development

## Slide 17: Thank You
someone@example.com